## Slide 1
Design of a Dual Automatic Door Control System with Optocoupler Isolation and Docking Charging Mechanism Based on Arduino Mega and ESP32
: YANUARDI
: 221344031
:Ir. Hertog Nugroho, M.Sc., Ph.D.
D4 TELECOMMUNICATIONS ENGINEERING ELECTRICAL ENGINEERING DEPARTMENTBANDUNG STATE POLYTECHNIC
2025
NAME
NIM
ADVISOR

## Slide 2
Background & Objectives
BackGround
  Automation Requirements: Drone stations require precise and secure moving –
  doors.Security Issues: Noise from high-torque motors risks damaging
  microcontrollers.IoT Integration: Wireless monitoring without delay is
  required.Charging: The charging mechanism must be automatic and secure (interlock).

## Slide 3
Background & Objectives
Objectives
  Synchronization: Adjusts two stepper motors with 2.
  precision timing.Charging: Automatic charging
  mechanism with interlock.Protection: Optocoupler
  isolation & limit switch for safety.IoT Monitor: ESP32 web server for real-time control.

## Slide 4
Time and Place of Implementation
This internship will be held on:
Date: July 1, 2025 to January 2, 2026
Time: 8:00 a.m. to 5:30 p.m. WIB (Western Indonesian Time)
Location: PT. Solusi Intek Indonesia
Company Location
At Workshop 08 Cikunir, located at Cikunir Raya No. 8, RT.004/RW.011, Jatimekar, Jatiasih District, Bekasi City, West Java 17422.

## Slide 5
THEORETICAL BASIS & IMPLEMENTATION

## Slide 6
Theoretical Basis: Controller
  Arduino Mega 2560
  Main control unit. Selected for its 54 I/O pins and 4 UART hardware. Handles motor and sensor logic.2.
  2.ESP32
  WiFi communication module. Functions as a standalone web server that sends commands to Mega via Serial.

## Slide 7
Theoretical Basis: Actuator
  HUIYINN Stepper MotorStrong
  holding torque to support door loads. Precise movement per step (1.8 degrees).
  2. B6600 DriverMotor
  current amplifier (up to 4A) with Microstepping feature for extremely smooth movement.

## Slide 8
Theoretical Basis: Protection
  PC817 OptocouplerIsolates the Arduino's 5V signal from the motor's 30V voltage using light. Prevents damage caused by Back-EMF.
  Limit SwitchMechanical limit sensor (NO) to detect the end position of the door and stop the motor automatically.

## Slide 9
Control Logic
  Non-Blocking (millis)
  Enables multitasking: the motor moves while reading sensors without a ‘delay()’ pause.
  2. Async Web Server
  The ESPAsyncWebServer library handles HTTP requests in the background without blocking the system.

## Slide 10
Hardware Assembly
  Preparation: Prepare Mega, ESP32, TB6600 Driver, and 30V Power Supply.
  PCB Prototype: Solder the Optocoupler and terminal block for a sturdy signal path.
  Wiring: Connect the Serial2 (Mega) communication path to Serial2 (ESP32).

## Slide 11
Pemrogramming & UI
  Mega Firmware: Motor logic and sensor interlock program with millis().
  ESP32 Web: Creating an HTML/CSS/JS interface stored in program memory.
  Serial Data: Protocol for sending real-time status from Mega to Web.

## Slide 12
TESTING & ANALYSIS

## Slide 13
Methodology & Testing
  1.
  Partial Testing: Motor, Limit Switch, Insulation
  2.
  Communication Test: UART ESP32 – ATMega2560
  3.
  Functional Testing: Synchronization & Charging
  4.
  IoT Test: Web Server Latency.

## Slide 14
Motor Performance Test
  Results & Analysis
  The OPEN_1/CLOSE_1 command is responded to correctly.
  Smooth Movement Due to TB6600
  MicrosteppingNo ‘Step Loss’ on normal door load

## Slide 15
Protection System Test
  Limit Switch
  The motor stops < 120 ms after the switch is pressed. Debounce works well to prevent signal bouncing.
  Optocoupler
  The signal is transmitted using light, so that Back-EMF or voltage surges from the motor will never damage the microcontroller.

## Slide 16
Communication Test
Test Item | Observation | Results
send command | Accepted in full by Mega | successful
Send Status | Real-time updates (500ms) | successful
Stability | No corrupt data | STABLE

## Slide 17
Synchronization Test
  OPEN_TOGETHER mode
  Motor 1 runs -> Pause 1300ms -> Motor 2 runs.
  CLOSE_TOGETHER mode
  Motor 2 runs -> pause1300ms -> Motor 1 .
  Precision timing is executed by millis().

## Slide 18
Synchronization Test Video

## Slide 19
WebUI Latency Test
  Findings
  There is a slight visual lag if the log data is too long, but it does not interfere with control functions.
  Respon Time
  150 – 300 ms
  Average time from button click to motor movement

## Slide 20
System Analysis
  Integration
  ATMega2560 and ESP32 work harmoniously to connect physical hardware and the web.
  Reliability
  The system is stable in long-term testing.No crashes

## Slide 21
System Conclusion
  Succesful Control : Dual automatic door system is functional and precise
  Effective Protection : Optocoupler & Limit Switch successfully protect hardware
  IoT Running : ESP32 Web Server is stable for real-time monitoring
  Ready to Use : Suitable for use as a docking station prototype

## Slide 22
Development Recommendations
  Upgrade Server
  Using the SIM800L and SIM7600 modules, automatic door systems can be controlled and monitored via a mobile application anytime, anywhere.
  Encoder Motor
  Add an encoder to the Closed-Loop system for absolute positioning

## Slide 23
Optimization Recommendations
  Protocol MQTT
  Implementation of Cloud IoT for remote access via the Internet.
  Watchdog Timer
  Enable watchdog for auto-restart if the system freezes.

## Slide 24
Thank You
  YANUARDI – 221344031